## Slide 1: EFI_PEI_SERVICES
Notes: Types of Documents: AMI Internal Only (INT)
Audience: AMI employees only
Cannot be distributed to any customer under NDA
Cannot be distributed as a public document
Found on internal servers only
Examples:
  Implementation guides
  Product plans & specifications
  Chipset Support Package (CSP) specification
  Employee training

## Slide 2: Agenda
EFI_PEI_SERVICES
  PPI Services
  Boot Mode Services
  HOB Services
  PEI Memory Services
  Reset Services
Reference documents:
Pre-EFI Initialization Core Interface Specification Version 0.9

## Slide 3: EFI_PEI_SERVICES
The PEI Services Table includes a list of function pointers in a table.
Struct
EFI_TABLE_HEADER | Hdr
PPI Functions | 
EFI_PEI_INSTALL_PPI | InstallPpi
EFI_PEI_REINSTALL_PPI | ReInstallPpi
EFI_PEI_LOCATE_PPI | LocatePpi
EFI_PEI_NOTIFY_PPI | NotifyPpi
Boot Mode Functions | 
EFI_PEI_GET_BOOT_MODE | GetBootMode
EFI_PEI_SET_BOOT_MODE | SetBootMode
HOB Functions | 
EFI_PEI_GET_HOB_LIST | GetHobList
EFI_PEI_CREATE_HOB | CreateHob
Firmware Volume Functions | 
EFI_PEI_FFS_FIND_NEXT_VOLUME | FfsFindNextVolume
EFI_PEI_FFS_FIND_NEXT_FILE | FfsFindNextFile
EFI_PEI_FFS_FIND_SECTION_DATA | FfsFindSectionData
PEI Memory Functions | 
EFI_PEI_INSTALL_PEI_MEMORY | InstallPeiMemory
EFI_PEI_ALLOCATE_PAGES | AllocatePages
EFI_PEI_ALLOCATE_POOL | AllocatePool
EFI_PEI_COPY_MEM | CopyMem
EFI_PEI_SET_MEM | SetMem
Status Code | 
EFI_PEI_REPORT_STATUS_CODE | ReportStatusCode
Reset | 
EFI_PEI_RESET_SYSTEM | ResetSystem

## Slide 4: EFI_PEI_SERVICES
Parameters
Hdr | The table header for the PEI Services Table.
InstallPpi | Installs an interface in the PEI PEIM-to-PEIM Interface (PPI) database by GUID.
ReInstallPpi | Reinstalls an interface in the PEI PPI database by GUID.
LocatePpi | Locates an interface in the PEI PPI database by GUID.
NotifyPpi | Installs the notification service to be called back upon the installation or reinstallation of a given interface.
GetBootMode | Returns the present value of the boot mode.
SetBootMode | Sets the value of the boot mode.
GetHobList | Returns the pointer to the list of Hand-Off Blocks (HOBs) in memory.
CreateHob | Abstracts the creation of HOB headers.

## Slide 5: EFI_PEI_SERVICES
Parameters
FfsFindNextVolume | Discovers instances of firmware volumes in the system.
FfsFindNextFile | Discovers instances of firmware files in the system.
FfsFindSectionData | Searches for the next matching file in the Firmware File System (FFS) volume.
InstallPeiMemory | Registers the found memory configuration with the PEI Foundation.
AllocatePages | Allocates memory ranges that are managed by the PEI Foundation.
AllocatePool | Frees memory ranges that are managed by the PEI Foundation.
CopyMem | Copies the contents of one buffer to another buffer.
SetMem | Fills a buffer with a specified value.
ReportStatusCode | Provides an interface that a PEIM can call to report a status code.
ResetSystem | Resets the entire platform.

## Slide 6: EFI_PEI_SERVICES
Introduction
A PEI Service is defined as a function, command, or other capability created by the PEI Foundation
during a phase that remains available after the phase is complete. Because the PEI phase has no
permanent memory available until nearly the end of the phase, the range of PEI Foundation
Services created during the PEI phase cannot be as rich as those created during later phases.
The following are PEI Services, which are described in this section:
PPI Services | Manages PEIM-to-PEIM Interface (PPIs) to facilitate intermodule calls between PEIMs. Interfaces are installed and tracked on a database maintained in temporary RAM.
Boot Mode Services | Manages the boot mode (S3, S5, normal boot, diagnostics, etc.) of the system.
HOB Services | Creates data structures called Hand-Off Blocks (HOBs) that are used to pass information to the next phase of the Framework.
Firmware Volume Services | Walks the Firmware File System (FFS) in firmware volumes to find PEIMs and other firmware files in the flash device.
PEI Memory Services | Provides a collection of memory management services for use both before and after permanent memory has been discovered.
Status Code Services | Provides common progress and error code reporting services (for example, port 080h or a serial port for simple text output for debug).
Reset Services | Provides a common means by which to initiate a warm or cold restart of the system.

## Slide 7: PPI Services
InstallPpi
ReInstallPpi
LocatePpi
NotifyPpi

## Slide 8: PPI Services

## Slide 9: PPI Services

## Slide 10: PPI Services

## Slide 11: PPI Services

## Slide 12: PPI Services

## Slide 13: Boot Mode Services
GetBootMode
SetBootMode

## Slide 14: HOB Services
GetHobList
CreateHob

## Slide 15: PEI Memory Services
InstallPeiMemory
AllocatePages
AllocatePool
CopyMem
SetMem

## Slide 16: Status Code Services

## Slide 17: Reset Services